## Slide 1
Peering Trend and Practice
Saw Yan Paing
CCIE #57005
MMIX | ARK Premium Solutions Limited

## Slide 2
Brief History of Internet
1960s
1990s
1980s
The Internet started in the 1960s as a way for government researchers to share information.
  Publishing “ARPANET” in 1967.
  Proposed line speed 2.4 kbps to 50 kbps.
  In 1969, it initially connected four universities' computers to each other.
In 1983, A new communications protocol was established called Transfer Control Protocol/Internet Protocol (TCP/IP).
  This allowed different kinds of computers on different networks to "talk" to each other.
  All networks could now be connected by a universal language.
  In 1989, Tim Berners-Lee, a British scientist, invented the World Wide Web (WWW).
In 1991, the Internet became available for public access.

## Slide 4
The Global Internet Peering Ecosystem
Tier 2 ISPs
Tier 1 ISPs
Content Provider
US Internet Region
Japan Internet Region
EU Internet Region
AU Internet Region
The Global Internet Peering Ecosystem consists of a set of interconnected internet regions (Countries).

## Slide 5
Tier 1 ISPs
Tier 1 ISP Model
Tier 1 ISP Peering Interconnections
Peering Motivation
  Tier 1 ISPs don’t pay transit fees, so they are only motivated to peer with each other as a way to provide connectivity for their customers.
  Generally, Tier 1 ISPs don’t want to peer with non-Tier 1 ISPs.
Peering Policy
  Most Tier 1 is seen as Restrictive Peering Policies.
Reference
Qwest - http://www.qwest.com/legal/peering_na.html
AT&T - http://www.corp.att.com/peering/
Verizon - http://www.verizonbusiness.com/terms/peering/

## Slide 6
Case Study
International Story. For example, a large international ISP built into Brazil and was able to negotiate peering with the dominant regional Tier 1 ISPs, with the argument that it did not represent a serious threat to their home market, and that the free access to its international customers would be beneficial. Once established in that region, the international ISP obtained transit contracts with a few customers within the region, and that traffic traversed the peering connection.
Telecom Italia. One exception to the Regional Tier 1 ISPs doesn’t peer rule exists in Italy. Telecom Italia is a formerly state-owned telephone company and Regional Tier 1 ISP in Italy. They peer openly in the region, preferring one interconnect point, but accepting multiple if the peer prefers. This is exactly the opposite of every story heard elsewhere in the world.
Source: drpeering.net

## Slide 7
Tier 2 ISPs
Tier 2 ISP Model
Peering Motivation
  Tier 2 ISPs motivate to peer in region to reduce the transits cost.
Peering Policy
  “Open” Peering or “Selective” Peering Policy
Reference
Example of Open Peering Policies
CAIW Netwerken - http://www.as15435.net/pp/
WISCNet - http://www.eng.wiscnet.net/peering/
NetAccess : http://www.nac.net/eng/peering.asp
Tier 2 ISPs need to purchase Transit to access some part of the internet regions.
Example of Selective Peering Policies
peer1 - http://www.peer1.com/infrastructure/peering.php
Bouygues Telecom - http://peering.as5410.net/
BT - http://www.bt.net/info/peering.shtml
EasyNet - http://www.noc.easynet.net/network/public/peering.php
AboveNet - http://www.abovenet.com/peering/
Comcast - http://www.comcast.com/peering/

## Slide 8
Content Provider
Content Provider Model
Peering Motivation
  SLAs w/well known ISP
Peering Policy
  “No Peering” Policy
Traditional content Provider : focuses on content development and does not Sell access the Internet.
Large Scale Network Savvy Content Providers : are the group of Content Providers that have adopted Peering as a strategy for lowering traffic expenses, increasing their ability to control and improve the end-user experience.
Peering Motivation
  Similar motivations to peer with Regional Tier 2 ISPs
Peering Policy
  “Open Peering” Policy

## Slide 9
Cable Companies , aka Broadband Internet Service Provider
Cable Company Model
Peering Motivation
  Similar to Tier 2 ISPs, motivate to peer to reduce transits cost, avoid Internet transits traffic congestion, better customer experience
Peering Policy
  “Open Peering” Policy
  The cable company are regional and don’t tend to compete in overlapping areas, and they tend to pull enormous volumes of traffic.

## Slide 10
The cable companies emerge as independent players.

## Slide 11
The Large-Scale Network-Savvy Content Providers peer openly.

## Slide 12
Content peers with eyeballs. The Tier 2 ISPs and the cable companies peer with the content companies that entered the peering ecosystem.

## Slide 13
Content peers with eyeballs. The Tier 2 ISPs and the cable companies peer with the content companies that entered the peering ecosystem.

## Slide 14
Transit price dropped an average of 30% per year.
Internet traffic has historically grown by 40–50% per year.
Global Internet Transit Price Trend
  “Internet Transit is so inexpensive, why do we need anything else?”

## Slide 15
  “Internet Transit is so inexpensive, why do we need anything else?”
  Without Peering, Packets will travel the Ocean. Twice!

## Slide 16
Advantages of Peering
Peering is significantly cheaper than IP Transit and will help you to reduce IP Transit costs.
Peering will give you direct access to many Content and Eyeball networks.
Peering leads to shorter AS paths and helps to improve your profile in a competitive market environment.
Peering allows direct control over the traffic flows.
Peering make the Internet robust and reliable.
Peering is where the Internet lives.

## Slide 17
Peering Rollout
Connect to Reginal IX
Define your own peering policy
Do not stop to explain to difficult to peer targets why Peering does make sense

## Slide 18
Peering Policies
”Open” Policy
Peer with everyone, regardless of type of provider
Mainly used by all kinds of Content Providers/Content Delivery Networks and many Tier 2, and Tier 3 Provider

## Slide 19
Peering Policies
”Selective” Policy
ISP will only peer with another ISP that does meet the prerequisites listed in a Peering Policy ( Example: Minimum traffic , Coverage, Number of routes announced)
Mainly used by bigger Tier 2 providers

## Slide 20
Peering Policies
”Restrictive” Policy
Peer with a very limited number of networks.
Typically don’t want to add more Peers

## Slide 21
Thank You